## Slide 1: Intel® Edison Workshop
Day 1, 5th December 2016
Lab 4 Level 3 School of Computer Science USM Penang 11800
Notes: NOTE: Finalize workflow for content as the final slide will be updated later.

## Slide 2: Switch to ‘Workshop’ account
Password: lab4workshop123

## Slide 4
We will provide a transport to school of Physics. Kindly gather at PSKOMP
Park you car at public parking space!

## Slide 5: F&B
BJIM, Level 5

## Slide 6: Intel® Edison Workshop
Day 1, 5th December 2016
Lab 4 Level 3 School of Computer Science USM Penang 11800
Notes: NOTE: Finalize workflow for content as the final slide will be updated later.

## Slide 7: IoT Development

## Slide 8: Developer track
Arduino
developer
JavaScript
developer
C/C++
developer
Visual
programming
Yocto Linux SPI
Arduino IDE
Win/Mac/Linux*
Arduino Sketch C++
Quark
(Galileo/Edison)
Arduino Libraries
Yocto Linux SPI
XDK
Win/Mac/Linux*
JavaScript
(Node.js)
Quark
(Galileo/Edison)
Intel XDK IoT Edition
Yocto Linux, Windows, WR Linux
Eclipse
Win/Mac/Linux*
C/C++
Quark, Atom, Core, Xeon
Intel System Studio Wind River*
Yocto Linux
Wyliodrin
Web
Visual Python
Quark
(Galileo/Edison)
Wyliodrin*

## Slide 9: Overview for developers
Hardwares
Software images
IDEs
Cloud Services
Intel XDK IoT Edition
Arduino IDE
Eclipse
Intel System Studio for IoT
Wyliodrin
+ Linux tools (GCC tool chains, drivers (Bluetooth, WiFi, etc), useful daemons like lighttPD and Node.js
Intel Analytics Dashboard
IBM Bluemix

## Slide 10: Expectation for this workshop
Intel Edison with Arduino* Expansion board
Grove Starter kit for Intel Edison
Notes: The focus of this Edison workshop is to use Intel Edison with Arduino* expansion board, and to experience some hands-on with Arduino Sketch programming and also Node.js for Intel XDK.

## Slide 11: Intel Edison
Compute Module
Small, Powerful and Adaptable hardware
Dual-core Intel Atom CPU 500MHz
Integrated Wi-Fi*, Bluetooth Low-Energy
32-bit Intel Quark microcontroller at 100Mhz
1Gb of RAM, 4Gb of storage
40 multiplexed GPIO interfaces

## Slide 12: Development kits
Intel provides two(2) development kits with Intel Edison compute module:
Intel Edison Arduino expansion board
Intel Edison Mini breakout board
a)
b)
Notes: Compute module (Intel Edison) alone is going nowhere unless you want to go the extreme way.
Intel has come out with Intel Edison development kit, which are Arduino expansion board and mini breakout board.
Why we need this? These development kits provides standard connectors and interfaces while supports wide range of possible prototyping of projects and easy-of-development for designing and building your products solution.

## Slide 13: Intel Edison
Arduino* expansion board
To provide better & easy IO interfaces and Arduino* compatibility
20 digital input/output pins (4 PWM outputs, 6 analog inputs)
1 UART(RT/TX)
1 I2C input connector
1 ICSP6-pin header (SPI)
Compatible with Arduino Uno R3
Hardware guide: http://www.intel.com/content/dam/support/us/en/documents/edison/sb/edisonarduino_hg_331191007.pdf
Notes: Officially, Intel provides two expansion boards to support interfaces for Edison:
  Arduino* expansion board – compatible with Arduino Uno R3 interfaces
  Mini-breakout board – small size factor

## Slide 14: Things you need to know
Intel Edison for Arduino Expansion board
MicroSD slot
DC barrel connector
USB port
Middle port – power over USB, Ethernet over USB, uploading Arduino program
Edge port – serial connection (access terminal)
Support Arduino I/O
The slider microswitch – configure Edison for Device/Host mode
Arduino* expansion board hardware guide:
http://www.intel.com/content/www/us/en/support/boards-and-kits/000005583.html

## Slide 15: Preparing Intel Edison development
Activity 1

## Slide 16: Tools (Pre-installed, ‘sw’ folder at Desktop)
Intel Edison Installer
Update firmware, set device name, set password, connect WiFi
Git Bash
Useful for transferring files (scp command)
Intel XDK
Official Intel editor for NodeJS IoT development (including HTML5 mobile app)
NodeJS
Run program locally and the use of NPM command.
MongoDB
MQTT Broker
PuTTY
Useful for serial connection and SSH

## Slide 17: Make sure you receive:
1x Intel Edison Arduino* expansion board
1 x Grove Indoor Environment Kit
1 x MicroUSB cable
1 x power adapter for Intel Edison
Write your name on top of Edison & Grove kit – avoid misplace & confused

## Slide 18: Step 1 - Connect Edison Module
Connect Intel Edison module into Arduino* expansion board.

## Slide 19: Step 2 - connect Edison to PC
The slider microswitch allows you to configure between USB Device mode and USB Host mode.
Device mode (toggled down) – turn Edison into computer peripheral and allow you to program the board over USB or mount onboard flash memory.
Host mode (toggled up) – allow USB peripherals (such as keyboard, mouse, camera, etc) to connect to Edison.
USB host mode requires the use of external power (adapter or battery).
Middle port is used for:
Power through USB
Ethernet over USB
Uploading Arduino sketches
Updating the firmware
Use power through DC (7-15V input DC power supply, or can be part of the battery pack) if you want power intensive features WiFi, servo motor or Arduino shields.
Step 1 – Make sure the microswitch is toggled-down.
Step 3 – Connect microUSB to PC
Step 2 – Power up your Intel Edison with DC Adapter.

## Slide 20: Step 3: Set Device name and password
1. Launch Edison Windows* installer.
2. Set device name and password by “Enable Security”.
Notes: This minimum setup allows you to work on Edison with full terminal access and WiFi through power over USB.

## Slide 21: Step 4: Connect to WiFi
3. Connect to WiFi access point “edison-training”
Access Point
edison-training: 3444555666777
cs-mtg-room: bilik703
Notes: This minimum setup allows you to work on Edison with full terminal access and WiFi through power over USB.

## Slide 22: Well done!
p/s: We are NOT encouraging you to update firmware since it may take minutes to complete due to heavy USM network usage during office hours.

## Slide 23: Simple Arduino IDE Sketch Programming
Activity 2

## Slide 24: Basics with Arduino IDE (Sketch Programming)
Arduino IDE is a development tool for writing a program (mostly known as a “sketch”) for Arduino* supported platform.
code section – this is where you write your sketch program
Compile – compile the sketch code into executable binary.
Upload – upload and run executable binary into Galileo.
Compilation console – details of compilation output will appear here, use for debugging purposes.
Serial Monitor – output serial from Galileo board, buffered back to PC.
Arduino IDE is designed to break the hurdle for artists, makers, newcomer in software development which provides a simple clicks for compile and upload the program therefore give more time to develop the idea and creativity in their project.
Notes: This will eventually gives more time for the newcomers to develop the idea and creativity in their projects rather than a complex tasking and details in software development.
But for experience developers, they can choose which way works for them.

## Slide 25: Basics with Arduino IDE (Sketch Programming)
Steps:
1. Write a program on Arduino IDE 2. Compile your code into executable binary
3. Upload the program into Edison
4. Run the sketch.

## Slide 26: Check-out Intel board on Arduino IDE
Check Windows* Device Manager to identify current working port (COM)
Notes: The screenshots show on how to check-out the development board that you are currently working with on Arduino IDE. Choose the correct Intel board and COM port in order to enable you to upload the sketch into Edison.
If Edison does not appear on the list, which means either you are working with fresh Arduino IDE or your Arduino IDE yet to support Intel platform, kindly open board manager (select “Tools” > “Board:” > “Boards Manager”) to install Intel specific board into Arduino IDE. Search Edison throughout the search box and click install to let Arduino IDE complete the process.

## Slide 27: Check-out Edison Port: COMX
1. Identify Edison Port COM by using Windows* Device Manager.
2. Choose COM port on Arduino IDE: Tools > Port

## Slide 28: Compile & Run
Notes: The screenshots specify on how to compile and upload your Arduino sketch into the board.

## Slide 29: Input/Output:
Input
Output
Identify your component either input or output

## Slide 30: Analog/Digital IO Pins
Analog pins (A0-A5) – Input
Digital pins (6 PWM = 3, 5, 6, 9, 10, 11) – Input/Output

## Slide 31: Activity: Deploy your sensor to Edison
In this activity, you will choose which sensor that you want to work with. Choose well since you will be working with that sensor till the end of workshop.
Grove Indoor Environment Kit
D2
D2
Notes: In this activity, participant will choose one sensor to work with their Edison. Later participant will assemble, connect, write and upload the sketch to Edison board. At the end of this activity, participant should be able to understand basics Arduino I/o pins connection and write simple sketch program, and compile/upload into the board using Arduino IDE.

## Slide 32: Basic Programming: Digital
pinMode
digitalRead
digitalWrite
Pull-up / pull-down resistor

## Slide 33: pinMode
Syntax: pinMode(pin, mode)
Pin: the number of pin whose mode you wish to set
Mode:
  Input
  Output
  Input_Pullup

## Slide 34: digitalRead
Syntax: DigitalRead(pin)
Pin: the number of digital pin you want to read(int)
Returns:
  HIGH
  LOW

## Slide 35: digitalWrite
Syntax: digitalWrite(pin, value)
Pin: the number of the digital pin you want to write (int)
Value:
  HIGH
  LOW

## Slide 36: Basic programming: analogRead
Syntax: analogRead(pin)
Pin: the number of analog input to read from (0-5)
Returns: Int (0 to 1023)
Scale: 0 to 1023 = 0V to 5V

## Slide 37: Basic programming: analogWrite(PWM)
Syntax: analogWrite(pin, value)
Pin: the pin to write to
Value: Int (0 to 255)

## Slide 38: PWM
Pulse Width Modulation: Output analog results with digital means
Digital control is used to create a square wave, a signal switch between on and off.

## Slide 39: Exercise: Button
Turn on the built-in LED on pin 13 when you press the button on pin D2
Use Arduino example
  File > Examples > 02.Digital > Button

## Slide 40: Step 1:
Connect Base Shield into Edison.
Connect Button to D2 on Base Shield.

## Slide 41: Step 2: launch Arduino IDE
Otherwise, download and install.
https://www.arduino.cc/en/Main/Software
Use Button Arduino example
  File > Examples > 02.Digital > Button

## Slide 42: Step 3: Check-out Intel board on Arduino IDE
Check Windows* Device Manager to identify current working port (COM)
Notes: If Intel Edison is not appear on the list (Tools > Board:), Kindly open Boards Manager (Tools > Board: > Boards Manager), and type ‘intel’ on the search box, and click Intel i686 Boards by Intel. Later click ‘Install’ button to install.

## Slide 43: Step 4: Check-out Edison Port: COMX
1. Identify Edison Port COM by using Windows* Device Manager.
2. Choose COM port on Arduino IDE: Tools > Port

## Slide 44: Step 5: Compile & Run Button example
Click ‘Verify’ to compile and check syntax error.
Click ‘Upload’ to run your sketch.
You should see the LED on the Edison turns on when you press the button.

## Slide 45: Code challenge 1: write Arduino* sketch for:
Grove Moisture sensor
Grove Light sensor
Grove PIR sensor
Grove UV sensor
Objective: to understand how to read from digital pins.
Checkout Arduino Sketch APIs here: https://www.arduino.cc/en/Reference/HomePage
Notes: Activity-3 refer code samples

## Slide 46: Introduction to Intel XDK
Activity 3

## Slide 47: Intel XDK IoT
Programming language: NodeJS
Current latest version: 3641
Not really stable. Otherwise developer is encouraged to develop project directly on Edison (ssh, serial, vim, command-line development)
Building IoT application and HTML5 mobile app
https://software.intel.com/en-us/intel-xdk-iot-edition-guide
Brackets*-based IDE for JavaScript* and HTML5 mobile applications.
Provides templates for creating new applications and remote debugging.
Notes: Install Intel XDK in your PC. Otherwise, download Intel XDK at: https://software.intel.com/en-us/intel-xdk

## Slide 48: Intel XDK IDE: Explained
This is your workspace panel. All files that you work will be listed here. Perform right click on the panel to create a new file.
1. Upload – upload current project on device. Resolve dependencies in package.json and install them on the device.
2. Stop – stop the project/process currently running.
3. Run – run project that is currently installed.
4. Debug – remotely debug the project.
5. Manage daemon / IoT device.
6. Connect to IoT device. Rescan to discover for devices or you can connect manually.
7. SSH Terminal - Allows you to connect your IoT device through SSH.
8. Serial Terminal – connect IoT device through serial connection.
1
2
3
4
5
6
7
9

## Slide 49: Intel XDK: Connect to Edison
Click Rescan for Devices to discover your Edison board.
Spot your Edison board appeared on the list. Default account is root. Just put your password and click Connect.
p/s: If everything goes wrong, you can add your Edison board manually but with the condition that you know the IP Address. Setup Serial connection and access command-line terminal and also use ifconfig to discover the IP Address. Then click Add Manual Connection to start connect.

## Slide 50: Intel XDK IDE: Running your project
Click Upload. This will upload your project and system will resolve all project’s dependencies from package.json.
Click Run to run your project. Checkout logs output from terminal to identify the issues for immediate bug fixes.
p/s: Kindly note that the default path of your XDK project in Edison is: /home/root/.node_app_slot

## Slide 51: Experience slow uploading…
As expected since the project is transferred via WiFi. If this irritates you then we suggest you start with traditional command-line style of development.

## Slide 52: Power intensive features
Connect DC power supply for power intensive features. This setup allows you to configure Edison into either Host mode or Device mode (use slider microswitch to toggle up or down). This setup extends Edison capability for rich development mode which make it easy to configure host/device mode without interrupting the board.
1
1
Kindly notice that the slider microswitch is toggled up to enable Host mode (connecting peripherals on USB port).
Notes: This setup actually allows you to configure Edison into USB Host mode (allowing for peripherals connection such as keyboard, mouse, camera etc) and USB Device mode for uploading Arduino sketches and connection to PC.

## Slide 53: IoT Development
Programming language: NodeJS
Libmraa
https://github.com/intel-iot-devkit/mraa
IO library: Libmraa
APIs: Aio(), Gpio()
APIs documentation
C/C++: http://iotdk.intel.com/docs/master/mraa/
Python: http://iotdk.intel.com/docs/master/mraa/python
NodeJS: http://iotdk.intel.com/docs/master/mraa/node
https://github.com/rwaldron/johnny-five
Galileo: https://github.com/rwaldron/galileo-io
Edison: https://github.com/rwaldron/edison-io
APIs documentation
http://johnny-five.io/api/
Examples – Grove IoT Kit
http://johnny-five.io/examples/
J5

## Slide 54: Some interesting libraries
Libmraa – use for IO communication(interface to pins) https://github.com/intel-iot-devkit/mraa
UPM – sensor library https://github.com/intel-iot-devkit/upm
Socket.IO – reliable communication https://github.com/socketio/socket.io/
Express – Node.js web framework https://github.com/expressjs/express/
galileo-io / edison-io – Intel Galileo/Edison IO plugin for Johnny-Five https://github.com/rwaldron/galileo-io
Mqtt – client library for MQTT protocol https://github.com/mqttjs/MQTT.js
MOSCA – mqtt broker https://github.com/mcollina/mosca
MongDB – MongoDB native driver https://github.com/mongodb/node-mongodb-native
Sqlite3 – SQLite bindings for Nodejs https://github.com/mapbox/node-sqlite3
Checkout NPM (Nodejs Package Manager) to find useful library. https://www.npmjs.com/

## Slide 55: Libmraa
Linux Library for low speed IO Communication in C with bindings for C++, Python, Node.js & Java. Supports generic io platforms, as well as Intel Edison, Intel Joule, Raspberry Pi and many more. http://mraa.io
PWM – not stable

## Slide 56: Libmraa: Code Sample
Include library
Hookup to I/O pin
Manipulate: read/write
var m = require('mraa');
console.log("Libmraa version: " + m.getVersion());
// moisture sensor at Analog pin A0
var moisture = new m.Aio(0);
setInterval(function() {
console.log("moisture: " + moisture.read());
}, 1000);
APIs Documentation: http://iotdk.intel.com/docs/master/mraa/node/

## Slide 57: Step 1: launch Intel XDK
Already pre-install in PC.

## Slide 58: Step 2: Use XDK to connect to Edison
Click ‘Rescan for Devices’ to discover your Edison board.
Choose your Edison board from the list in order to connect. Retain ‘User name’ as ‘root’, enter your password and then click ‘Connect’.

## Slide 59: Step 3: Connect Grove Sensors
Code sample is available at ‘2016-edison-workshop/day-1/code-challenge-2/’ directory and check which pin should the moisture sensor is connected to. You may use other pins as the code sample only provide simple guidelines on how to start.

## Slide 60: Step 4: Create new project with Intel XDK
Click ‘START A NEW PROJECT’ and choose ‘Blank IoT Node.js Template’.
Name your project as ‘moisture’.
Copy moisture sensor code (main.js) from ‘grove-indoor-environment-kit-nodejs/01-moisture’ directory into main.js of your XDK project.

## Slide 61: Step 5: Upload your project
Click ‘Upload’. This will upload your project into Edison board. Later, the system will resolves dependencies which specified from your package.json.

## Slide 62: Step 6: Run your project
Click ‘Run’ to run your project.
Observe output from terminal logs.
Click ‘Stop’ to stop the program.

## Slide 63: Code Challenge 2: Write Nodejs JavaScript program for:
Moisture sensor
Light sensor
PIR sensor
UV sensor
Objective: Understand IO bindings of Libmraa

## Slide 64: Johnny-Five
https://github.com/rwaldron/johnny-five
Galileo: https://github.com/rwaldron/galileo-io
Edison: https://github.com/rwaldron/edison-io
APIs documentation
http://johnny-five.io/api/
Examples – Grove IoT Kit
http://johnny-five.io/examples/
Code example: Johnny-Five + Intel Edison + Grove Moisture sensor
J5
Notes: Introduction to Johny-five

## Slide 65: Code Challenge:
Johnny-Five
1: Grove – Button
2016-edison-workshop/day/1/code-challenge4/j5button.js
sample
2: Grove – Servo
2016-edison-workshop/day/1/code-challenge4/j5servo.js
sample
Kindly notice that Johnny-five APIs is written specifically for one particular sensor. Kindly checkout the documentation for details.
Code sample is available at ‘day-1/code-challenge-3/j5’ directory and check which pin should the moisture sensor is connected to. You may use other pins as the code sample only provide simple guidelines on how to start.
Turn on the built-in LED on pin 13 when you press the button on pin D2 using Johnny-Five IO.
Turn on the built-in LED on pin 13 when you press the button on pin D2 using Johnny-Five IO.

## Slide 66: Commands and useful tools

## Slide 67: Establish Serial connection to Edison
Step 1 – Make sure the microswitch is toggled-down.
Step 3 – Connect the second microUSB port to PC for Serial Connection
Step 2 – Power up your Intel Edison with DC Adapter.

## Slide 68: Use Intel XDK > Serial Terminal tab to start serial connection to Edison.

## Slide 69: Use PuTTY for Serial Connection
Launch PuTTY
Choose ‘Serial’
Set Speed to ‘115200’
Set Serial line to your Edison USB Serial Port (check device manager)
Click ‘Open’ to start access Edison terminal.

## Slide 70: SSH – Secure Connection (remote access)
Launch PuTTY
Choose ‘Serial’
Set ‘Host Name (or IP Address)’ to your Edison IP Address.
Click ‘Open’ to start SSH connection.

## Slide 71: Common *nix commands
Yocto: Based on
Try out these commands in your terminal.
BusyBox
https://www.busybox.net/

## Slide 72: Set device name, password and WiFi connection.
$ configure_edison --setup // full setup: devicename, pass, WiFi
$ configure_edison --wifi // configure WiFi
$ configure_edison --name // configure device name
$ configure_edison --password // configure password
$ configure_edison --help // see more details

## Slide 73: Ifconfig: discover ip address
$ ifconfig

## Slide 74: Install packages
OPKG commands
$ opkg update // update packages list
$ opkg install <package> // install a package
$ opkg remove <package> // remove a package
$ opkg list | grep <package> // search for a package

## Slide 75: Task Manager Alternative: top/htop
To start, type ‘top’
To exit, type ‘q’
$ top

## Slide 76: Check Disk Space
$ df -kh

## Slide 77: Enable Drivers
$ modprobe <driver>
e.g: $ modrobe uvcvideo // enable video driver (webcam)

## Slide 78: GPIO
Software vs Embedded Engineer Perspectives
Build a system or application with simple plug&play sensors/shields
Edison I/O pins
Library/APIs
Linux command-line tools
(hardware) Edison board
More functionality and control with IO pins
Manage IO pins at software level
Manage IO pins (directly) at hardware level
Code sample: https://github.com/intel-iot-devkit/mraa/blob/master/examples/javascript/Blink-IO.js
set pin 13 to output (write)
set pin A0 to input (read)
List of GPIOs path: /sys/class/gpio/

## Slide 79: Check kernel changes
Useful for seeing hardware changes
$ dmesg | tail -9
Try connect peripherals

## Slide 80: Disable Arduino Functionality
$ systemctl disable clloader // disable Arduino programming
$ systemctl enable clloader // enable Arduino programming
$ systemctl stop clloader // stop
$ systemctl start/restart clloader // start or restart
$ systemctl status clloader // check current status for clloader
your sketch are stored here: /sketch/sketch.elf

## Slide 81: Add Repository
# Path Repository for packages
/etc/opkg/
Specify your repository in /etc/opkg/ directory so that you can get your desire packages for the development.
AlexT repo (non-official)
http://alextgalileo.altervista.org/edison-package-repo-configuration-instructions.html
src/gz all http://repo.opkg.net/edison/repo/all
src/gz edison http://repo.opkg/net/edison/repo/edison
src/gz core2-32 http://repo.opkg.net/edison/repo/core2-32
Intel repo (official) 3.5
http://iotdk.intel.com/repos/
src all http://iotdk.intel.com/repos/3.5/iotdk/edison/all
src edison http://iotdk.intel.com/repos/3.5/iotdk/edison/edison
src core2-32 http://iotdk.intel.com/repos/3.5/iotdk/edison/core2-32
Notes: Edison repository for software packages. The shown example of Intel repo is version 3.5. You may used older version. Kindly checkout http://iotdk.intel.com/repos.

## Slide 82: Command-line Editors
Vi/Vim
Nano

## Slide 83: Command-line development: Best practices
Default path for your XDK project: /home/root/.node_app_slot

## Slide 84: Command-line development: Best practices
Vi/Vim/Nano Editor
Notes: Vi/Vim/Nano is one of the best command-line editor. You need to ensure that you know a few cheats (how to write, how to save, etc) so that you are comfortable the next time writing programs in command-line editor.

## Slide 85: Command-line development: Best practices
Resolve dependencies: /$ npm install –save
Run NodeJS program: /$ node main.js